Mexican Beetle 1600i Engine Bay 28 pin Connector Information:-

Connector Location:-

1600i Engine Bay 28 pin Connector Layouts:-

Engine Bay End (wire view)		     Bodywork End (wire view)

1600i Engine Bay 28 pin Connector Pinout:-

Pin #	Purpose							Wire Colour

1 	Fuel Injectors (+)						Red

2 	Fuel Injectors (Ground)						Black

3 	Cylinder Head Oil Temperature Sensor				Brown or

Brown/Red

4 	Ground connections for the following:-				Brown/White

- Oil Temperature Sensor

- Air Intake Temperature Sensor

- Hall Sensor (pin 1)

- Throttle Potentiometer (pin 3)

5 	Positive connection for the following (to approx 1997):-		Black

- Idle Speed Stabiliser

- Magnetic Valve

- Ignition Module (pins 3, K-Line and 15 ??)

Note: This pin is not connected on later vehicles.

6 	Ignition Module (pin 2, Signal)					Green/Black

7 	Lambda Sensor (pin 1, Signal)					Black

8

9	Lambda Sensor Heater ground					Brown or

Brown/White

10 	Oil Pressure Switch						Green/Red

11

12 	Activated Charchol Filter Valve					Green/Yellow

13 	Hall Sensor (pin 2, Signal)					Green/Black

14 	Hall Sensor (pin 3, +)						Red/Black

15 	Throttle Potentiometer (pin 1)					Blue

16 	Throttle Poteniometer (pin 2)					Green/Red

17 	Ignition coil power output stage					Brown

18 	Alternator Voltage Regulator (D+)				Blue

19 	Air Intake Temperature Sensor					Lilac/Black

20 	(not connected)

21 	Lambda Sensor Heater (pin 3, +)				White

22

23 	Reverse (back up) light switch					Black/Grey

24 	Right reverse light						Black

25 	Left reverse light						Black

- connects to T28/4 (see current flow diagram)

- To c. 1997 – not connected

From c. 1997 – Magnetic Valve (N80)				Black/Yellow

28 	(not connected)

Mexican Beetle 1600i 28 pin Connector – Installation/Removal:-

# The photo below (on the left) shows the engine bay connector locked correctly in place:-

Connector installed.			      Connector being unplugged.

To unplug the engine bay connector from the body’s wiring harness, do the following:-

-    Disconnect the ground from the battery

- Turn the small ring anti-clockwise as shown in the above right photo.

- Keep un-doing the small ring until the engine wiring harness can be disconnected from the body’s wiring harness.

Re-installation is the reverse of removal.  Make sure that the notches align correctly as shown in the above left photo.

This document was originally written in German on the 1600i website and has been written in English (in my own words) by Phil Ade, Tuesday 27th June 2006.